| INFORMATION |  |
| --- | --- |
| Question | How do I setup a Guest Wi-Fi Network in my DG2460/70 A Gateway? |

| Answer | The DG2460A allows for a guest Wi-Fi network (in addition to the primary Wi-Fi network). The guest Wi-Fi network provides access to the Internet, but prevents devices from communicating with the primary Wi-Fi and wired connected client devices. The DG2460A broadcasts two different guest Wi-Fi networks independently over the 2.4 GHz and 5 GHz radio bands. 2.4 GHz devices can only connect to the 2.4 GHz Wi-Fi network, and newer devices that support 5 GHz can connect to either the 2.4 Ghz or 5 GHz Wi-Fi network. The Guest Wi-Fi networks are limited to 32 users and disabled by default. This document describes how to setup the Guest Wi-Fi network. Guest Wi-Fi Network Setup Launch a web browser, such as Internet Explorer, Firefox, or Safari. Enter http://192.168.0.1 into the address box, and press the Enter key. The Login page will appear. NOTE: A security or private risk alert may appear on the web browser advising users to proceed with caution when accessing the Web Manager. There is no risk in proceeding to the Web Manager. On the Login page, enter admin in the User Name field. Enter password or a customized password in the Password field. Click the Apply button. The System Basic Setup page will appear. On the System Basic Setup page, click the Wireless 2.4 GHz link on the top menu. The System Basic Setup page will appear. On the left-hand menu, click the 2.4GHZ Guest SSID link. The 2.4GHz Guest Setup page will appear. Check the EnableGuestWireless box to enable the 2.4 GHz Guest Wi-Fi network. Enter a new wireless network name in the Wireless Network Name (SSID) field. Enter a new wireless password in the Pre-Shared Key field. Click the Security Mode drop-down menu to select the encryption type to use. Open (None Secure) - Network security is not set for the Wi-Fi network. This allows access to the Wi-Fi network without a Wi-Fi Security key. WEP (64/128) (Poor Security) - Wired Equivalent Privacy, older network security standards (not recommended). WPA/WPA2-PSK (TKIP/AES) (Most Compatible) - Combination of Wi-Fi Protected Access version 2 with Pre-Shared Key and Wi-Fi Protected Access with Pre-Shared Key. WPA2-PSK (AES) (Recommended) - Wi-Fi Protected Access version 2 with Pre-Shared Key. ​​​Click the Apply button. NOTE: To enable the 5 GHz Guest Wi-Fi, click the Wireless 5 GHz link on the top menu, then click the 5GHZ Guest SSID link on the left-hand menu, and repeat steps 7 - 11. |
| --- | --- |

***Tip

***If this is a modem swap, it is suggested that you change the guest SSID and password to match the previous setup, then the guests will not need to change their settings on any of their devices.  They will connect with no setup needed for new gateway.

This can be done for main Wi-Fi setup also.